Off Road Driven!

www.procompusa.com

2360 Boswell Road, Chula Vista, CA  91914

Phone: (619) 216-1444 		Fax: (619) 216-1474

TECHNICAL BULLETIN

BULLETIN #: 57086B / 57087 / 57088 Fender Flares

DATE: 2/18/2016

RE: Wide Fender Flare kit for K5150B / K5151B

PART #: 57086B / 57087 / 57088

This is a comprehensive performance kit that requires unique procedures outside of the normal remove and replace components.  Pro Comp strongly recommends following the advice provided on the page 5 introduction.

This bulletin provides additional information for the successful installation of the Tundra Long Travel Suspension kits K5150B / K5151B.

If you have received a 57086BMX-6 packaged 9/23/15, without CV axle boot bands, hardware pack 90-60605, contact Pro Comp customer service 800-776-0767 and the hardware bag will be sent UPS Red Label.

Wide fender flare kits, front pn 57087 and rear pn 57088 are for 2014-2016 models and include front marker lights for the grill, front and rear side marker lights, center rear lights, wire, snap plugs and small OD washers for flare installation.    Hardware packages with 36) 1.0” OD fender washers will be sent to replace the small diameter washers provided for fender flare installation.  A revised front light bracket will also be included to address trim levels that may not accept the provided 84-10246 bracket.

The front marker lights tie into the factory side marker leads.  Wire the center lights in sequence from the factory driver side marker light.  Use yellow wire from LED to factory green wire for power / white to white for ground.  The rear marker lights tie into the license plate harness.  Use red wire from LED to factory green wire for power / white to white for ground.  Connectors to tie the LED wires into the factory wires are not provided.  Scotch Lock wire splice connectors can be used

A final note on sway bar installation, step 116 of the instructions states; cut off the corner of the bracket.  This will be revised to state; cut / remove material from the ends of the sway bar to provide a flush mount to the 35-10227 and 35-10229 sway bar end link brackets.  Material may also need to be removed from the lower edges of the sway bar to allow the end link brackets to mate flat against the sway bar.