TECHNICAL BULLETIN

BULLETIN #: 05UPF250SW

DATE: 1/12/2016

RE: 05-16 Ford F250 / F350 4WD Vehicles with Steering Wheel Oscillation

In monitoring our technical service inquiries and technical service bulletins from Ford, there is the potential for moderate to severe steering wheel oscillation (wobble) to occur.   After extensive testing and outside feedback, the following details have been established to correct or prevent steering wheel oscillation occurrences in lifted 05-16 Ford Super Duty 4wd pickups:

Alignment: recommended caster settings between 2.5 to 3.5 degrees.

Pro Comp p/n 599, eccentric adjusters will be needed to make

caster adjustments, since the factory upper ball joint inserts do not 			       offer provision for adjustment.

Steering and Suspension components: worn out shock absorbers (lack sufficient 			       damping), loose or worn out tie rods, ball-joints and track bar can 			       contribute to a steering wobble.

Make certain these parts are within service limits.

It is also critical that the pitman arm nut is tightened to the

torque specification of 350 ft/lbs.

Tire Pressure: will be subject to specific owners load requirements, tire 			       	       choice and factory tire pressure sensor specifications.

Proper adjustments to tire pressure can also reduce the 			       	       tendency to wobble.  Example: Pro Comp 35 x 12.50 -18 Xtreme A/T

with E load range has a maximum pressure recommendation of 			       65psi for maximum load requirements.  Under normal operating

conditions without load, 50psi is sufficient.

Dual Steering Stabilizer: a properly installed dual stabilizer kit will provide the 			       final defense against potential steering wheel wobble.  Use Pro 			       Comp p/n 222582 or 222582Z.

Please contact our Customer Service Tech Department at (800)-776-0767 or

(619)-216-1444. They will be able to assist you with any questions you may have in regards to this issue.

PRO COMP SUSPENSION

2360 BOSWELL ROAD

CHULA VISTA, CA. 91914

TOLL FREE: (800)-776-0767 PHONE: (619)-216-1444 FAX: (619)-216-1474

WWW.PROCOMPUSA.COM