www.explorerprocomp.com

Suspension Systems That Work!

2360 Boswell Road, Chula Vista, CA  91914

Phone: (619) 216-1444 		Fax: (619) 216-1474

DATE: 2.11.08

RE: Drive Shaft Lubrication

APPLICATION: All EXP Drive Shafts

WHY LUBRICATE?

Proper lubrication of any moving parts in a driveline is essential to keep the driveline in proper working order and to obtain an acceptable service life.

WHAT SHALL I LUBRICATE?

All universal joints, slip yoke and stub shaft assemblies, as well as centering kits in CV heads should be greased regularly.

HOW?

Universal Joints

Secure grease gun on grease fitting and pump in grease until all four bearings are lubricated. To check for this, make sure that all four seals have purged out air and old grease. Grease until fresh grease appears at the base of all four seals. If a seal does not purge properly, move the driveline to free up the end clearance of the bearing cup. On bearing plate style U-joints, it may necessary to loosen the bolts two or three turns to allow grease to flow. If the joint still does not grease properly, disassemble the kit to determine the source of the problem.

Slip Yoke and Stub Shaft Assemblies

Before putting the slip yoke onto the stub shaft, coat both parts uniformly with a layer of grease. After assembly, but before installation into vehicle, fully collapse the driveline and apply grease to the grease fitting until it comes out of the vent hole in the welch plug. Cover the hole and continue greasing until grease appears at the seal.

At relubrication it may be impossible to fully collapse the driveline. Follow the same general greasing procedure but be careful not to overfill. Overfilling may cause the welch plug to pop out during operation.

Centering Kits

A special needle nose grease gun adaptor is needed to grease the flush type fitting on centering kits. Apply grease until fresh grease appears at the purge hole or at ball seal.

WHEN SHALL I LUBRICATE?

Frequency of lubrication is determined by the type of service which the driveline is subject to. A list of recommended relube cycles for various conditions is shown below:

Service Conditions		Re-Lube Period		Approximate Miles

City				Every 3 Months			6500

Highway			Every 1 Month			12,000

Off-Highway			Every 3 Months			6,500

Line Haul			Every 1-2 Months		20,000-30,000

Off Highway 4x4		Every Month			2,500

WHAT TYPE OF GREASE SHOULD I USE?

A good quality Lithium Complex soap type lube EP (extreme pressure) grease, with an NLGI grade of 1 or 2, is recommended.

Thank You,

Engineering Department